## Slide 1
System Design using Verilog
Contents of the lecture
User Defined Primitives (UDP)
Some Rules of UDP
UDP of Two input AND gate
UDP of Two input OR gate

## Slide 2
User Defined Primitives (UDP)
UDP are used to define custom verilog primitives by using Look up Tables
UDP can specify:
(i) Truth table of combinational circuits
(ii) State table of sequential circuits
(iii) Don’t care, rising edge, falling edge can be specified

## Slide 3
User Defined Primitives (UDP)
For combinational circuits the truth table entries are specified as:
<input 1> <input 2> <input 3> ……… <input n> : <output>;
Some Rules for UDP
The inputs to a UDP can only be scalar
Multiple inputs can be used
The inputs are declared by keyword “input”
Input entries in the table must be in the same order as the “input” list
The output to a UDP can only be one
The output must appear first in the terminal list
For combinational UDP the output terminal must be declared by “output”
For sequential UDP the output terminal must be declared by “reg”

## Slide 4
primitive and_2 (y,a,b);
input a,b;
output y;
table
// a b : y
0 0 : 0;
0 1 : 0;
1 0 : 0;
1 1 : 1;
endtable
endprimitive
Use of Don’t care
primitive and_2 (y,a,b);
input a,b;
output y;
table
// a b : y
0 ? : 0;
1 0 : 0;
1 1 : 1;
endtable
endprimitive
UDP of Two input AND gate
For combinational circuits the truth table entries are specified as:
<input 1> <input 2> <input 3> ……… <input n> : <output>;

## Slide 5
UDP of Two input OR gate
primitive or_2 (y,a,b);
input a,b;
output y;
table
// a b : y
0 0 : 0;
0 1 : 1;
1 0 : 1;
1 1 : 1;
endtable
endprimitive
For combinational circuits the truth table entries are specified as:
<input 1> <input 2> <input 3> ……… <input n> : <output>;